## Slide 1
Should hale-core write GeoParquet?
What GeoParquet is, how it connects to hale-core,
what the spike in spikes/geoparquet-poc actually does —
and the decision we need to make.
ING-5399 · INVESTIGATION SPIKE
Notes: Thanks for making time today.
This presentation is about a short research task – a "spike" – under ticket ING-5399. The question behind it is simple: should hale-core be able to save data as GeoParquet files?
I've split the session into two parts. In the first part I'll explain what GeoParquet is, how it would fit into hale, and what we found out when we tried it. I'll start from the beginning, so you don't need any background. If something is unclear, please interrupt me and ask.
In the second part, at the end, we decide together what happens next.
One important thing to keep in mind: this was research, not product work. Nothing you'll see today goes into hale as it is. The spike was a small experiment to answer one question: is this worth building properly? That's the decision we're here to make.

## Slide 2
2
Agenda Where we’re going?
01
What is GeoParquet
02
How it connects to hale-core's existing architecture
03
Inside the spike: a file-by-file code walkthrough
04
What was actually verified — including two real corrections
05
The case for and against building it
06
Next steps
Notes: Here's the plan for today, in six steps.
First, what GeoParquet actually is – explained from zero, no background needed.
Second, how it would fit into hale-core. The short version: it's not a new kind of thing for us. It follows the same pattern as export formats we already have.
Third, a look inside the spike: what we built and how it works. I'll keep the technical parts short.
Fourth, what we found when we ran it – including two mistakes we made along the way and fixed. I think those are useful to see.
Fifth, the arguments for and against building this for real.
And sixth, the next steps – the decisions I'd like us to take before we leave the room.

## Slide 3
3
What is GeoParquet?
A convention for storing geospatial vector data (points, lines, polygons) inside a plain Apache Parquet file — not a new file format. Parquet is a columnar binary format (used a lot in the data/analytics world — DuckDB, Spark, etc.) that's great for compact storage and fast column-based queries. GeoParquet just says: "here's how to put geometries in a Parquet column and describe them so geo tools know what they're looking at.“
Why it exists: Before GeoParquet, sharing large vector datasets meant Shapefile (old, limited) or GeoPackage (SQLite-based, row-oriented). GeoParquet gives you Parquet's benefits — compression, columnar access, huge ecosystem (DuckDB, pandas, Spark, etc.) — for spatial data.
How a geometry actually gets stored:
Encoded as WKB (Well-Known Binary) — the same binary geometry format JTS/GeoTools already use internally.
Put into a column, one geometry per row, like any other Parquet column.
Extra metadata describes the geometry column: its CRS, what geometry types appear (Point/Polygon/etc.), a bounding box, etc.
Notes: Let's start with the basics: what is GeoParquet?
GeoParquet combines two things. The first is Parquet. Parquet is a file format for tables of data – rows and columns, like a big spreadsheet. It's the standard format in the data and analytics world. Tools that data teams use every day – DuckDB, Spark, pandas – read and write it directly.
What makes Parquet special is how it stores the table: column by column, instead of row by row. Imagine a huge spreadsheet where you only care about one column. With Parquet, a tool can read just that column and skip everything else. That makes searching very fast, and it also compresses very well, so the files are small.
The second thing is geometries – points, lines and polygons – together with their coordinate reference system, the CRS, which says where on Earth the coordinates are. That's what we work with in hale every day, for example in GML.
GeoParquet simply says: here is the agreed way to put geometries into a Parquet file, so that every tool understands them the same way.
Why does that matter? Until now, if you wanted to share a large map dataset as a file, you mostly had two choices: Shapefile, which is old and has many limits, or GeoPackage, which is good but stores data row by row, like a classic database. GeoParquet brings Parquet's advantages – small files, fast queries and many tools – to map data.
And a nice detail for us: inside the file, each geometry is stored in a standard binary format called WKB – Well-Known Binary. hale already produces WKB today, using a library called JTS (Java Topology Suite) . So there's no new geometry format to learn.

## Slide 4
4
What is GeoParquet?
A convention for storing geometries inside a plain Apache Parquet file — not a new file format.
• Geometry → WKB. Well-Known Binary, the same encoding JTS/GeoTools already use, stored one geometry per row.
• 1.x approach: geometry lives in a plain BINARY column; ALL the spatial meaning (CRS, encoding, geometry types) is bolted on separately as a JSON blob in the file's key-value metadata (a "geo" field). The column itself looks like nothing special to a generic Parquet reader.
• 2.0 approach (what we need). Parquet itself gained native GEOMETRY / GEOGRAPHY logical types — the column is self-describing at the format level.
• GeoArrow — dropped in 2.0. Good news for us: no Apache Arrow dependency required.
• CRS as PROJJSON. Richer, machine-readable CRS description — a writer needs a CRS → PROJJSON path.
GeoParquet 1.x
BINARY column
+ "geo" JSON metadata carries everything
GeoParquet 2.0 — target
BINARY column + native GEOMETRY logical type
"geo" metadata layered on top
Notes: The important point on this slide: there are two versions of GeoParquet, and the difference really matters for us.
Version 1. Here, the geometry is stored in a completely ordinary column of raw bytes. Everything that says "this is geometry, and this is its coordinate system" is written separately, in a small JSON note in the file's metadata. A normal Parquet tool that doesn't know the GeoParquet rules just sees a column full of meaningless bytes.
Version 2, is the one we need. Since last year, Parquet itself has a built-in type for geometry, called GEOMETRY. So the column itself says "I contain geometry", and any Parquet tool can recognise it, even without knowing the GeoParquet rules. The JSON note still exists on top, for more detailed information like the exact coordinate system.
Two more points. First: there was a competing idea called GeoArrow – storing geometries in the format of another library, Apache Arrow. It was dropped in version 2. That's good news for us, because Arrow is a big, heavy library we wanted to keep out of hale.
Second: the coordinate system – the information that says where on Earth our coordinates are. Usually we identify it with a short code, like EPSG:2056 for Switzerland. That's like saying "recipe number 2056": you need the cookbook to know what it means. GeoParquet wants the full recipe inside the file – written out as JSON, called PROJJSON – with the Earth model, the projection and the axes. That way any tool can read it, without needing its own cookbook. hale doesn't produce that today. For the spike, we download it from a public website, spatialreference.org, and keep a copy. That can't ship – exports would fail without internet – so for production we'd ship those definitions with the plugin instead.

## Slide 5
5
How it connects to hale-core
hale-core already has a family of geo export plugins that follow one shape.
InstanceWriter
interface
AbstractInstanceWriter
common/plugins/.../instance/io/impl
AbstractGeoInstanceWriter
implements GeoInstanceWriter
GeopackageInstanceWriter
existing, shipped
What this means in practice
• The existing GeoPackage writer already does: read hale's Instance / GeometryProperty / CRSDefinition → convert CRS via GeoTools → encode geometry to WKB via JTS → write.
• A future GeoParquetInstanceWriter would follow the exact same shape — identical up through “encode to WKB,” then hand those bytes to parquet-java instead of GeoPackage's API.
• This spike proves that last step works standalone. It is deliberately NOT wired into hale's Instance model yet — that's follow-up scope.
Notes: This slide should be reassuring: GeoParquet would not be a new kind of thing in hale. It fits a pattern we already use.
In hale, every export format is a "writer" – a piece of code that takes hale's data and saves it as a file in a certain format. All writers are built in layers, like a family tree. At the top is InstanceWriter – the general rule that every export follows. Below it are shared building blocks, and one of them, AbstractGeoInstanceWriter, adds everything needed for map data: geometries and coordinate systems. All of this exists today.
One of the writers built on it is our GeoPackage export, which users already have. I looked at what it does. In four steps: it takes the geometry and coordinate system from hale's data, converts the coordinate system with a library called GeoTools, turns the geometry into WKB bytes with JTS, and then writes the file with the GeoPackage library.
A GeoParquet writer would be a sibling of the GeoPackage writer. The first three steps would be the same. Only the last step changes: instead of handing the WKB bytes to the GeoPackage library, we hand them to the Parquet library.
That last step is the new part – and that's exactly what the spike tested, on its own, outside hale. Connecting it to hale's data model is not part of this spike; that would be the follow-up work.

## Slide 6
6
The write pipeline, end to end
Read the data
GeoPackage row
JDBC + header strip
Encode shapes
WKB bytes
JTS WKBWriter
Label as geometry
Parquet column
native GEOMETRY type
+ "geo" metadata
Save the file
.parquet file
GeoParquet 2.0
Check it
DuckDB
schema + round-trip check
The only step older GeoParquet 1.x writers didn't need to get right.
In a real hale plugin, step one becomes hale's own Instance / GeometryProperty / CRSDefinition model — the same shape the existing GeoPackage and Shapefile writers already read from. Everything from step two on is unchanged.
In plain words: data goes in on the left, a checked GeoParquet file comes out on the right. Only the highlighted step is new.
Notes: Before we go into the details, here is the whole idea in one picture. Data goes in on the left, and a checked GeoParquet file comes out on the right. Let me walk through the five boxes.
One: read the data. For the test, we read map data from an existing GeoPackage file.
Two: encode the shapes. Each geometry is turned into WKB bytes, the standard binary format, using JTS – the same library hale already uses.
Three: label it as geometry. The bytes go into a Parquet column, and the column gets the built-in GEOMETRY type, plus the JSON note with the coordinate system. This is the highlighted box, and it's the only really new step. Version 1 writers never needed it.
Four: save the file. The result is a .parquet file that follows GeoParquet 2.0.
Five: check it. We use a separate tool, DuckDB, to open the file and confirm that everything came out correctly.
And the connection to hale: in a real hale plugin, only the first box changes. Instead of reading from a GeoPackage file, we'd start from hale's own data – the same starting point our GeoPackage and Shapefile exports already use. Everything from box two onwards stays exactly the same. That's why it made sense to test the pipeline on its own first.

## Slide 7
7
In plain words: the spike does three jobs – write a GeoParquet file, try it on real data, and let an independent tool check the result.
What's actually in the spike folder
pom.xml
Standalone Maven build. parquet-hadoop with snappy-java / zstd-jni excluded (native codecs, unnecessary for uncompressed output).
CrsUtil.java
Downloads + caches PROJJSON per EPSG code. Spike-only – a real plugin would ship these definitions instead.
GeoParquetPoc.java
The core demo — 3 synthetic features written with the native GEOMETRY logical type.
GeoPackageToGeoParquet.java
Reads a real GeoPackage layer over JDBC, hand-parses its binary geometry header, writes via the same path.
validate.py
Independent DuckDB check: validates the “geo” metadata against the official JSON Schema and reads geometries back as WKT.
data/013_Grindelwald.gpkg
Real Swiss geological survey data, EPSG:2056, 18 layers — not synthetic samples.
NOTES.md
The full investigation log this deck distills.
Notes: This is what's actually in the spike folder in our code repository. You don't need to remember the file names. What matters is that the spike does three jobs: it writes a GeoParquet file, it tries that on real data, and it lets an independent tool check the result.
For the developers, a quick tour.
pom.xml is the build setup. It's a separate, standalone project, not part of hale's normal build. It deliberately leaves out two compression libraries, snappy-java and zstd-jni. They contain native code – code compiled for specific operating systems, not pure Java – and we don't need them for uncompressed files.
CrsUtil.java is the coordinate-system shortcut I mentioned earlier. It downloads the full PROJJSON description for each EPSG code and keeps a local copy. That's only for the spike – a real plugin would ship these definitions instead of downloading them.
GeoParquetPoc.java is the core demo. It writes three made-up shapes – a point, a line and a polygon – as a GeoParquet 2.0 file.
GeoPackageToGeoParquet.java does the same with real data: it reads an actual GeoPackage file and writes it out as GeoParquet.
validate.py is our independent check, using DuckDB.
data/013_Grindelwald.gpkg is the real test data – a Swiss geological survey dataset, not something we made up.
And NOTES.md is the full investigation log. This presentation is a summary of it, so if you want the details – exact error messages, lists of dependencies – that's where to look.

## Slide 8
8
GeoParquetPoc.java — the core mechanics
The schema line that makes a column actually GeoParquet-2.0-compliant:
.required(BINARY)
.as(LogicalTypeAnnotation.geometryType(crsIdentifier))
.named("geometry")
• Writes 3 synthetic features: point, line, polygon.
• Encodes geometry to WKB via JTS's WKBWriter — same encoder hale already uses elsewhere.
• Attaches a "geo" JSON file-metadata block (CRS, geometry types) alongside the native column type.
• Runs on parquet-hadoop with PlainParquetConfiguration — zero org.apache.hadoop.* classes touched at runtime.
Why this line matters
• GeoParquet 1.x wrote WKB into a plain BINARY column and put ALL spatial meaning in file metadata.
• 2.0 requires the column itself to carry Parquet's native GEOMETRY logical type — discovered mid-investigation, not assumed from the start.
• This was a real compliance gap in the spike's first version, not a nice-to-have.
In plain words: this one line labels the column as “geometry”. Without it, the file looked fine – but wasn't really GeoParquet 2.0.
Notes: This is the only piece of code in the presentation, and it's the most important line of the spike.
For everyone, an analogy: think of a moving box. In version 1, the box had no label. To know what was inside, you had to find the packing list, which was kept somewhere else. In version 2, the box itself says "geometry" on the outside. This line of code is that label.
For the developers: it defines a binary column named "geometry" and marks it with Parquet's built-in GEOMETRY type, including the coordinate system. That mark is what makes it a real GeoParquet 2.0 column – not just a column of bytes that happens to contain WKB.
The rest of this file writes the three test shapes, encodes them with JTS, adds the JSON note, and runs without Hadoop. Hadoop is a large big-data framework that we don't want inside hale – I'll come back to it on the findings slide.

## Slide 9
9
GeoPackageToGeoParquet.java — proving it on real data
• Reads a real GeoPackage layer over plain JDBC (org.xerial:sqlite-jdbc) — used only to load test input, not part of the write-path footprint.
• Hand-parses GeoPackage's binary geometry header (magic bytes, flags, SRS id, optional envelope) directly from the OGC spec to get at the raw WKB underneath.
• Feeds those bytes through the exact same writer as the synthetic demo — no separate code path.
• Test data: Bedrock_PLG layer, Swiss geological survey, EPSG:2056 (CH1903+ / LV95).
1,097
real polygon features
2.77 MB
uncompressed output
14
text attribute columns, incl. UUIDs + non-ASCII
0
Hadoop classes touched at runtime
All 1,097 rows read back correctly — including non-ASCII attribute text like “Aalénien” — through DuckDB, independently of this spike's own writer code.
In plain words: we didn't stop at made-up examples – real Swiss geology data went in, and all 1,097 rows came out correct.
Notes: we tested with real data.
This part of the spike reads an actual GeoPackage file. There's one technical trick: GeoPackage stores each geometry with a small extra header in front of the WKB. We removed that header, following the official GeoPackage specification, so we were left with plain WKB. Then we sent it through exactly the same writing code as the demo – there's no special path for real data.
The test data is a real layer called Bedrock_PLG – bedrock areas – from a Swiss geological survey dataset, in the Swiss coordinate system EPSG:2056.
The numbers on the right tell the story. 1,097 real polygons were written. The file is 2.77 megabytes, without compression. Each feature has 14 text attributes, including IDs and texts with French and German accents – like "Aalénien". That's a good test, because special characters are often where things break. And zero Hadoop classes were needed while running.
Then the most important part: all 1,097 rows were read back correctly by DuckDB – a tool we didn't write and have no influence on. So it's not our own code telling us that our own code works.

## Slide 10
10
What running it actually taught us
FIXED
Plain WKB wasn't 2.0-compliant
The obvious approach (WKB + file metadata only) is the old 1.x convention. Fixed once found — no library upgrade needed.
RISK
Compression drags Hadoop back in
Every codec except UNCOMPRESSED — GZIP included — makes parquet-hadoop construct a real Hadoop Configuration internally.
FIXED
OSGi bundling needed real testing
Built an actual bundle with hale's own tooling. Found hard, unresolvable imports on Hadoop/Snappy/Zstd — fixed by marking them optional.
OPEN
One more manifest fix, unapplied
Parquet's own relocated Jackson classes aren't declared private — small, mechanical, identified but not done.
CONFIRMED
Real data, not just synthetic samples
1,097 real polygons with non-ASCII text round-tripped correctly through an independent reader.
OPEN
CRS string convention unverified
The native logical type's crs field is left undefined by the spec itself — not checked against a reference writer yet.
Notes: I think this is the most important slide, because it's not just a list of things that went well. It's an summary of what we learned by actually running the code – including two corrections to our own earlier work. There are six cards, each marked Fixed, Risk, Open or Confirmed.
Fixed – plain WKB wasn't 2.0-compliant. That's the missing-label story from the code slide. Found, fixed, and no newer library version was needed.
Risk – compression brings Hadoop back. This is the one to remember. Hadoop is a large framework from the big-data world. We don't want it inside hale, because it's big and brings many other libraries with it. The Parquet library can run without Hadoop – but only as long as we write uncompressed files. As soon as we switch on any compression, even the simple GZIP, the library needs Hadoop again. So today: no Hadoop means no compression, and the files are bigger than they need to be. For the follow-up there are three options: ship uncompressed first, accept Hadoop as a dependency just for compression, or write our own small piece of code that compresses without Hadoop.
Fixed – plugin packaging. hale is built from plugins, using a system called OSGi, and each plugin has to declare exactly what it needs. Instead of assuming the Parquet library would fit, we actually built a plugin package with hale's own tools. It declared hard requirements on Hadoop and the compression libraries, which would have stopped the plugin from starting. We marked those as optional, and that fixed it.
Open – one more small packaging fix. The Parquet library contains its own internal copy of another library, Jackson, and that copy isn't declared correctly. We know the fix; we just didn't apply it in the spike.
Confirmed – real data. That's the 1,097 polygons from the previous slide.
Open – the coordinate-system text. The built-in GEOMETRY type has a field for the coordinate system, but the Parquet rules don't say what exactly should go in it – a short code, a full description, or something else. I haven't checked yet how other tools fill it in.

## Slide 11
11
Pure-Java, non-Arrow options compared
Option | License | Verdict
parquet-java (direct) | Apache-2.0 | Recommended — this spike
Carpet (com.jerolba) | Apache-2.0 | Not recommended — quietly needs hadoop-common
tileverse-io/parquetry | Apache-2.0 | Promising, unusable now — needs Java 25
GeoTools GeoParquet DataStore | LGPL-2.1 | Disqualified — read-only
GDAL / OGR | MIT-style | Disqualified — native/JNI dependency
Apache Sedona | Apache-2.0 | Disqualified — Spark/Flink-only runtime
All permissively licensed except GeoTools (LGPL-2.1 — already how hale-core consumes GeoTools elsewhere, not a new constraint). License wasn't the differentiator here — fit and maturity were.
Notes: Before recommending an approach, more alternatives have been looked into. I was not looking for just any library: the ticket asked for something pure Java – so no native code – and without the heavy Arrow library. Here are the six options.
parquet-java, used directly: the official Java library for Parquet, from the Apache project, free to use under the Apache 2.0 licence. This is what the spike is built on, and it’s what I would recommend.
Carpet: a friendlier layer on top of parquet-java. Its documentation says it doesn't need Hadoop. We checked its actual dependencies, and it does – it needs hadoop-common. It also doesn't add anything specific to GeoParquet. So: not recommended.
Parquetry: a newer library built specifically for GeoParquet, which sounds perfect. But it needs Java 25, and hale runs on an older Java version today. So we can't use it now – but it's worth watching for later.
GeoTools: a library hale already uses a lot. It can read GeoParquet, but not write it – and writing is what we need. Disqualified.
GDAL: the best-known toolkit in the geo world, and the most complete GeoParquet implementation. But it's native code, not Java, which goes against the goal of keeping hale pure Java. Disqualified.
Apache Sedona: only runs inside big-data platforms like Spark or Flink. It can't be built into an application like hale. Disqualified.
On licences, since the ticket asked about them: everything here is permissively licensed – free to use in our product – except GeoTools, which is LGPL. But hale already uses GeoTools under that same licence, so nothing changes. In the end, the licence wasn't what decided it – fit and maturity were.

## Slide 12
12
The case for and against
FOR BUILDING IT
• Real, not theoretical. Pure Java, no Arrow, validated against the actual 2.0 spec text.
• Fits hale's existing pattern exactly. Same shape as the GeoPackage/Shapefile writers already in the codebase.
• OSGi bundling is solved, not new. hale already has a proven shadow+bnd convention; this spike confirmed it works here too.
• Small, bounded dependency footprint.
• Proven against real, representative data, not just a synthetic sample.
• Permissively licensed. No new legal review needed.
REASONS TO PAUSE
• No compression story. Files ship uncompressed until the Hadoop-coupling in parquet-hadoop's codec factory is solved.
• CRS handling isn't production-ready. PROJJSON is fetched from a public website at runtime right now.
• Two OSGi manifest details still open before a real plugin build resolves cleanly.
• The crs field convention is a guess until checked against a reference writer.
• The spec is still a release candidate (2.0.0-rc.1), not final.
• No convenience library helps yet. The metadata/schema work is hand-rolled either way.
• Two more gaps: no bbox column, no CRS-without-EPSG path.
Notes: Now the actual decision material. I'll go through both sides without giving my opinion.
Arguments for building it.
It's real, not theoretical: the spike actually writes files, in pure Java, without Arrow, checked against the official 2.0 rules.
It fits hale's existing pattern exactly – the same shape as our GeoPackage and Shapefile exports, so there's no new architecture to design.
The plugin packaging is a known problem with a known solution. hale already has a way of doing this, and the spike showed it works here too.
The extra libraries we'd bring in are small and under control.
It's been tested with real data, not just a toy example.
And the licences are permissive, so no new legal review is needed.
Reasons to pause.
No compression yet: without Hadoop, files have to be uncompressed for now, so they're bigger.
The coordinate-system handling isn't ready for production – right now it downloads definitions from a public website.
Two small packaging details are still open.
What goes into the coordinate-system field of the GEOMETRY type is still our best guess.
The GeoParquet 2.0 specification is still a "release candidate" – an almost-final draft, not the official final version. It could still change.
No library does the GeoParquet-specific work for us – we'd write that part ourselves.
And two small gaps: we don't yet write the optional bounding-box column, which some tools use to find data faster, and we don't yet support coordinate systems that have no EPSG code.

## Slide 13
13
Where ING-5399 stands against its own Definition of Done
✓
Written library comparison (maturity, license, OSGi/JTS fit)
✓
A recommendation for the follow-up implementation
✓
Small PoC on real data, validated by an independent tool
✓
Documented open questions / risks for the follow-up ticket
All four DoD items are met. What's left is process: getting this in front of the team (this deck, plus NOTES.md) and a 16h time-box gut-check given how much ground this covered.
Caveat on that third item: only DuckDB has actually validated the output so far — a second attempt via GDAL/pyogrio was inconclusive for environment reasons (no Parquet driver in either build tested), not a finding about the file itself. Worth re-running with a full GDAL build before final sign-off.
Notes: Quickly: where does the ticket stand compared to what it asked for? The ticket had four conditions for being "done".
One: a written comparison of the library options, looking at maturity, licence and fit with hale – done; that's the options slide.
Two: a recommendation for the follow-up work – done; you'll see it on the last slide.
Three: a small proof of concept with real data, checked by an independent tool – done.
Four: a documented list of open questions and risks for the follow-up – done; that's the findings slide and the reasons to pause.
One honest remark on point three. So far, only one independent tool, DuckDB, has checked our files. We also tried a second one, GDAL, but in both versions we had access to, the part of GDAL that reads Parquet wasn't installed. So that test didn't fail – it simply couldn't run. That's a problem with our test setup, not with our files. Still, it would be good to repeat it with a complete GDAL installation before we call this fully closed.
So all four conditions are met. What's left now isn't more research – it's a decision to make.

## Slide 14
14
• Do we accept the open risks (compression, CRS convention, the two OSGi fixes) as scope for a follow-up implementation ticket — rather than blockers to starting one?
• Is uncompressed-only output acceptable for a first shipped version, given no pure-Java compressed path exists today?
• Who owns closing the two known, bounded OSGi manifest fixes before a real plugin build?
• Does the CRS/PROJJSON story (currently a network fetch, not shippable) need solving before or during the follow-up ticket?
• Are we comfortable building against a spec that's still officially a release candidate (2.0.0-rc.1)?
The decision we need
Notes: This is the part where I need you to talk, not me. There are five questions. Let's take them one at a time and try to agree on an answer for each before moving on
Question one: are the open risks work to plan in, or reasons not to start?
We've seen three open risks today. First, compression: without Hadoop, we can only write uncompressed files for now.
Second, the coordinate system: the spike downloads the descriptions from a website, and we still need to check what other tools write into the coordinate-system field of the GEOMETRY type.
Third, two small packaging fixes for the plugin.
What they have in common: we know what the problem is, and we know at least one way to solve it. None of them is a question where we don't know where to start.
So the question is: do we put them into the follow-up ticket as planned tasks, with an owner? Or does anyone think one of them is serious enough that we should wait?▎▎
Question two: is a first version without compression acceptable?▎▎ Compressed files are smaller – often much smaller. But today, the only way to compress with this library would bring Hadoop into hale, and we don't want that. So a first version would write uncompressed files.▎▎ To give you a sense of size: our test with 1,097 polygons produced a 2.77 megabyte file. For bigger exports, the files grow accordingly. The files are still completely valid and every tool can read them – they just take more space and take longer to download.▎▎ So: is that good enough for a first release, with compression added later? Or we need compressed files from day one? If it's the second, the follow-up ticket gets bigger.▎▎
Question three: who takes care of the two packaging fixes?▎▎ hale is built from plugins, and each plugin has to declare exactly which other libraries it needs. We found two small problems with how the Parquet library declares this. One is already solved in the spike; for the other, we know exactly what to change.▎▎
Question four: does the coordinate-system problem need solviw-up?▎▎ Right now, the spike gets the full coordinate-system descriptions by downloading them from a public website. That's fine for a test, but it can't ship: exports would fail without internet, or if the website change descriptions with the plugin.▎▎ The question is about timing. Do we want this solved and tested first, before the follow-up ticket starts – as a small preparation task? Or is it fine▎ to solve it as part of the follow-up ticket itself?
Question five: are we comfortable building on a specification that isn't final yet?▎▎
GeoParquet 2.0 is officially a "release candidate" – an almost-final draft. Usually that means only small changes happen before the final version, but it's not guaranteed. If something changes, we might have to adjust our writer later.▎▎ On the other side, the requirement is specifically for version 2.0, so waiting for the final version would also mean waiting to deliver. That's a question about how much risk we accept, and it's more a business decision than a technical.

## Slide 15
15
No pure-Java, non-Arrow alternative beats it today: Carpet adds an API layer without solving anything GeoParquet-specific, and Parquetry — the one library built for this — needs Java 25, which hale doesn't run yet. The open items aren't reasons to stop — they're exactly what the follow-up ticket should be scoped around.
Move forward with parquet-java direct —
with the risks scoped into the next ticket, not solved by it.
Notes: So here is my recommendation: go ahead with parquet-java, used directly, as the approach. And plan the open risks we discussed into the follow-up ticket – as part of its scope, not as reasons to wait.
Why do I think that's right? First, there's no better pure-Java option today. Carpet adds a nicer interface, but it doesn't solve anything GeoParquet-specific, and it isn't really free of Hadoop. Parquetry is the one library made for exactly this, and I'd definitely look at it again later – but it needs a Java version we don't use yet.
Second, every open point we've seen today is understood and limited in size: compression, the coordinate-system field, the two packaging fixes. None of them is an open-ended unknown. That's exactly the kind of risk that belongs in a well-planned ticket – not a reason to stop before we've started.
Everything I've shown today, with much more technical detail, is written up in NOTES.md in the spike folder, under ticket ING-5399, if anyone wants to go deeper after the meeting.
Thank you – and let's make sure we've agreed on those five decisions before we finish.

## Slide 16
16
Thank you
Notes: So here is my recommendation: go ahead with parquet-java, used directly, as the approach. And plan the open risks we discussed into the follow-up ticket – as part of its scope, not as reasons to wait.
Why do I think that's right? First, there's no better pure-Java option today. Carpet adds a nicer interface, but it doesn't solve anything GeoParquet-specific, and it isn't really free of Hadoop. Parquetry is the one library made for exactly this, and I'd definitely look at it again later – but it needs a Java version we don't use yet.
Second, every open point we've seen today is understood and limited in size: compression, the coordinate-system field, the two packaging fixes. None of them is an open-ended unknown. That's exactly the kind of risk that belongs in a well-planned ticket – not a reason to stop before we've started.
Everything I've shown today, with much more technical detail, is written up in NOTES.md in the spike folder, under ticket ING-5399, if anyone wants to go deeper after the meeting.
Thank you – and let's make sure we've agreed on those five decisions before we finish.